## Slide 1: Remote Metal Detection System
By Jay Wei
Prof. Jiang
Ens491

## Slide 2: Objective
The purpose of this project is to develop an metal detection system that allows operator to perform metal detection remotely.

## Slide 3: System Overview
Detection Circuit utilizes LC tank to continuously transmitting a signal
Frequency of signal to be received and measured by an remote receiver
The receiver will send frequency value to the PC via serial communication port for further processing

## Slide 4: Specifications
The system shall operate when metal detector is up to 30 feet from the operator
The metal detector will have detection depth up to 10cm below ground
The metal object to be detected shall be bigger than size of a quarter
The software shall be able to capture the location of metal detector upon detection of metal with < 1 second delay.

## Slide 5: Technical Detail - Metal Detection Circuit continuous
Complete metal detection circuit

## Slide 6
Simulation
Technical Detail - Metal Detection Circuit continuous

## Slide 7: Technical Detail -Frequency Receiver and counter
Signal to be received by RF receiver module.
DC bias added to make the signal digitally measurable by Arduino digital pin.
Amount of DC biasing to be determined based on actual received signal

## Slide 8: Project Scheduling

## Slide 10: Technical Detail -Arduino Frequency Measurement
Coding Approach :
Arduino UNO ATMega328 microcontroller equipped with 3 timer/counter registers (TCCR)
TCCR can be configured to received external clock source which can be our signal
To count the frequency, Output Comparison register (OCR) can be configured to decrement by 1 every clock cycle (cycle of our signal).
Then by measuring the time interval between each time the OCR reaches 0, we can calculate the frequency by dividing max number in OCR (255 for 8 bit) by time interval.
FrequencyCounter library

## Slide 11: Technical Detail -Object Tracking
Coding Approach:
The goal is to track the metal detector on a camera and mark its location accordingly
To trigger the marking of the detector’s current location, we set a threshold for the frequency. When frequency reach out of the threshold, the location of the detector at that specific moment is captured.
Background Subtraction Technique
  In computer vision, image/frame is represented by matrix (size to be determined by pixels).
  Each element of matrix hold (3) 8 bit values (0-255) each represents Red, Green , Blue. ie (255,255,255) represent white.
  Computer first capture frame1 as background, and then frame2 with object is introduced.
  Subtracting Frame2 by Frame1 will produce a Difference-Frame
  Difference-Frame holds the information about the location of the object
  By continuously subtracting new frame by frame1 as camera is recoding, object can be tracked
OpenCV library

## Slide 12: Cost Analysis – Budget
Estimation based on pricing from AMAZON
Major purchases:
  Arduino UNO R3 18.90
  433 mhz transmitter and receiver 5.00
  197’ 24AWG magnet wire 7.45
Minor purchases:
  Resistor, Capacitor, Transistor, AA battery 10.00
Total 41.35

## Slide 13: Risk Analysis and Mitigation
The signal received by receiver will not be exactly the same as the signal transmitted.
However, adjustment to circuit and program can be made to adopt the deviation.
If the deviation is too severe, then it might be more practical to measure the frequency at the detection side using additional microcontroller and transmit only frequency value instead of entire signal.

## Slide 14: Deliverable
Upon completion of project, live demo will be given in the classroom.
A completed project will consist of
  (1) metal detector with transmitter
  (1) Arduino with receiver circuit (+ frequency counter program)
  (1) Laptop connected to Arduino (+ object tracking program via webCam)
A successfully project has to satisfy all functional specification listed in slide 6 and produce the resulting image as shown in slide 5